## Slide 1: Collision Avoidance Procedures
The Devil is in the Detail
Harry Wilson, Baker Hughes (presenter)
Gary Skinner, Baker Hughes

## Slide 2
SPE 184730, Collision Avoidance Management and Principles
  WPTS’s recommended best practice
  Basis of the Collision Avoidance section of API RP78
Collision Avoidance Procedures

## Slide 3
SPE 184730, Collision Avoidance Management and Principles
  WPTS’s recommended best practice
  Basis of the Collision Avoidance section of API RP78
Detailed implementation must result in a robust procedure ensuring reliable outcomes
Procedures are dependent on, and must align with, Well Planning and Survey procedures
Collision Avoidance Procedures

## Slide 4
The biggest problem with Procedures is compliance
Mandating isn’t enough
Compliance must be facilitated
  Keep as simple as possible
  Align software with procedures
  Train
  Coach
Collision Avoidance Procedures

## Slide 5
Drilling Industry trends:
  ops coordination by generalists
  rig site down-manning/remote operations
  drilling automation
Robust procedures more necessary than ever:
  reduce subjective decision making
  automate via software
Even greater emphasis on planning
Collision Avoidance Procedures

## Slide 6
Walk-through of a service company Procedure:
Typically more detailed than Operator procedures
The detail is the glue that holds the process steps together
  and helps ensure reliable outcomes
Collision Avoidance Procedures

## Slide 7
Contract Award
Agree on JOP/Bridging Document
Collision Avoidance Procedures

## Slide 8: Planning Phase
Identify and manage collision risk with known offsets
Create a plan that allows Directional Driller (DD) to meet CA objectives
  DD’s won’t drill planned trajectory exactly, so manage drilling off-plan
HSE Risk ACR forms basis for all other rules:
  Non-HSE risk, Risk Assessment, Offset selection
Stop Drilling ACRs are probability based
  Define MASD
Available Space (ADP) defines “drillability”

## Slide 9: Scanning Rules
The reference well
+

## Slide 10: Scanning Rules: HSE Stop Drilling ACR
HSE risk Stop Drilling
Everything else relates to this rule.
+

## Slide 11: Scanning Rules: Stop Drilling ACRs
HSE risk Stop Drilling
Non-HSE risk Stop Drilling
+
3σ
3.5σ

## Slide 12: Scanning Rules: Stop Drilling ACRs
HSE risk Stop Drilling
Non-HSE risk Stop Drilling
. . . but deviation from Plan while drilling may bring other Offsets in to play.
+
3σ
3.5σ

## Slide 13: Scanning Rules: Offset well selection
Non-HSE risk Stop Drilling
HSE risk Stop Drilling
Offset well selection
+
50m/164ft

## Slide 14: Scanning Rules: Drilling Off Plan
Non-HSE risk Stop Drilling
HSE risk Stop Drilling
Risk Assessment (planning)
[Active Monitoring (drilling)]
Offset well selection
+
10m/33ft
Accommodates 10m off Plan.
The customer must risk assess each Offset that fails this rule.

## Slide 15: Limit rules to those required

## Slide 16: Multiple Views of the problem

## Slide 17: Proximity Risk Workbook

## Slide 18: Proximity Risk Workbook

## Slide 19: Collision Avoidance Programme
Instructions to the Directional Driller or Remote Ops Engineer
Equivalent to the Survey Programme

## Slide 20: Execution Phase
Focus is on:
  1. Can we drill the next stand down safely
  2. Are we more than 10m off plan
  3. Are we heading into a tight spot

## Slide 21: Auto-clearance function
Clearances are run automatically
  Immediately a survey is appended to the survey log
  When look ahead projection parameters are changed
Two ACRs applied over two projection intervals
  To current survey bit depth
  To next survey station bit depth

## Slide 22: Auto-clearance function

## Slide 23: Auto-clearance function

## Slide 24: Auto-clearance function

## Slide 25: Visualisation

## Slide 26: Reporting and Auditing
How do you prove that you were doing clearance scanning in real time?
  Store full clearance reports for each survey?
  Manually record survey and clearance statistics in a log?
  What look-ahead projections were used?

## Slide 27: Reporting and Auditing
Auto-clearances recorded automatically:
Formatted version with basic information
CSV version containing all data for detailed review
XML of raw data for archive
With Remote Ops and Automation being adopted due to Covid-19 do we want to define a WITSML object based around the Status Summary Report?

## Slide 28
Back to the JOP/Bridging Document
Collision Avoidance Procedures

## Slide 29
Service Company Procedures
Supported by aligned software, training and competency programme
Collision Avoidance Procedures
Training
Competency
Procedures
Software

## Slide 30
Danger of Joint Operating Procedures
Collision Avoidance Procedures
Training
Competency
Procedures
Software

## Slide 31
JOPs/Bridging Documents
Collision Avoidance Procedures
Perhaps the roles should be reversed

## Slide 32
10. Danger of Undetected Errors
Compliance with our Wellbore Positioning standard operating procedures minimizes the risk of well collision.
The procedures include actions specifically intended to identify errors and allow timely corrective action. However, no procedures are foolproof.
Therefore, our last line of defense against a wellbore collision is vigilance at the rig site.
Post Script

## Slide 33
An example procedure has been used to illustrate how some of the desirable features of a Collision Avoidance procedure might be realised:
  be easily understood
  minimise manual implementation
  minimise decision making at the rig site
  be automated in software where appropriate/possible
Thought should be given to the optimum form of Joint Operating Procedures
  avoiding possible loss of process integrity
Summary